## Slide 1: Elevator-Assisted Data Collection for High-rise Structures
Dan Wang
Department of Computing,
The Hong Kong Polytechnic University

## Slide 2: Sensor Data Delivery
Long-range, single-hop data transmission
  Simple, but not efficient
Short-range, hop-by-hop data transmission
  Our study: “Traffic-aware relay node deployment for data collection in wireless sensor networks”
  Cannot fully balance the load and energy consumption
The intrinsic problem is the long span of the structure
Both one-hop long-range and hop-by-hop short-range data transmission suffers when the scale of the structure expands
We propose to use elevators to assist sensor data collection
  The communication range will not increase when the structure expends!

## Slide 3: Experiment Verification
Results:
  Elevator movement 1.5 m/s
  Data transmission rate easily reach 55KB/s or higher
The encountering time is the most important
How to avoid insulation effect of the elevator compartment?
The No 2. elevator
Sensor mote
The sink (base station)

## Slide 4: A Formal Look at the Problem
A structure with n floors
One static sensor node on each floor
  Nodes on adjacent floors can communicate with each other
One sink node attached to the elevator
  Sink could collect data from sensor node on the same floor
Data collection in rounds
  Each round each sensor generate α bits of data
  Note: each round may be a few hours
  Data should be delivered no later than L rounds
Objectives
  Collect data on time
  Maximizing system lifetime

## Slide 5: The Scope of our Study
  The elevator is used for carrying passengers: we cannot control the elevator
  The elevator may stop at some floors: larger amount of data can be transmitted
  The elevator may not go to some floors for a long time
How to schedule the data flow?
A theoretical study from the network flow perspective
  We only work on scheduling of data traffic (flows)
  Assume MAC layer handles the interference
  Assume mechanism for reliable data delivery

## Slide 6: Treatment of the Problem
  The offline scenario: assume the elevator movement is known in advance
  Problem 1: Maximizing throughput (in one round)
  Problem 2: Maximizing minimum residual energy (in one round)
  Problem 3: The general case
The online scenario
  The difficulty
  A heuristic algorithm

## Slide 7: Problem 1: Maximizing Throughput
A Graph
Vertices
  s: a virtual source node
  d: sink node
  S: Sensor nodes
Edges
Edge Capacity
  αi the data generated by node vi
  βi the throughput from vi to d
  Comment: βi can be calculated by the duration the sink interact with vi × throughput
Observation: Equal to a max-flow problem; optimal solution exists

## Slide 8: Problem 2: Maximizing Minimal Residual Energy (MMRE)
Split node vi into two virtual nodes
Link capacity
  Green: Amount of data to be transmitted
  Red: Energy of sensor node
  Purple: Throughput to sink
Observation: Transform to a decision problem that can be solved by max-flow augmenting path algorithm; optimal solution exists

## Slide 9: Problem 3: The General Case
Taking L into consideration
Commodity<si,ti,Σα>
  Transmission schedule for the data generated in the ith round
Maximizing system lifetime
  Maximize the number of commodities
Observation: A multi-commodity flow problem; optimal solution exists

## Slide 10: The Online Scenario
Online algorithm is difficult
  Theorem: No online algorithm can have a transmission schedule that achieves a constant competitive ratio as opposed to the optimal offline algorithm
  Proof (non-trivial): the intuition is online algorithm performs arbitrarily bad if a balanced elevator movement followed by a non-balanced movement followed by a balanced movement

## Slide 11: Online Algorithm
Huge gap between offline algorithm and online algorithm
  Offline optimal, online arbitrarily bad
Is prediction of elevator movement possible?
  No need to predict exact movement
  Only aggregate throughput
Algorithm Design Sketch
  Assume know future period of T
  Dynamic adjustment

## Slide 12: Simulations
The operation of the elevator (Markov Chain)
  Move to another floor with probability p
  Or stay at the same floor for Ts time
Elevator movement model
  D&N model
  DAY model
  Tower model
  Office model
Default values
  Data rate 2Mb every 2 hours
  Data deadline 4 hours
  Predictable period 1 hour
  p = 10%
Comparison with hop-by-hop routing

## Slide 13: Simulation Results
Much better than hop-by-hop routing
Longer prediction period better performance

## Slide 14: Thank you!