## Slide 1: Flashback: Decoupled Lightweight Wireless Control
Asaf Cidon, Kanthi Nagaraj, Sachin Katti
Stanford University
Pramod Viswanath
University of Illinois at Urbana-Champaign
Notes: research on cloud and mobile systems
Google Israel
Katti的另一个学生：无线通信
Picasso: Flexible RF and Spectrum Slicing
Decouple 去耦（解耦）：比如数据通道中同时携带控制信息，这两种信息是无干扰的 称为 去耦

## Slide 2: How to Schedule a Wireless Network?
VoIP
File Sync
Notes: 基站

## Slide 3: Cellular: Decoupled Control Plane
Data Plane
Control Plane
Control Plane
Data Plane
You go first
Data data data data
You go second
Data data data data
I want to transmit sync
I want to transmit VoIP
Cellular networks pay high price for centralized control
VoIP
File Sync
Notes: 同步的过程 协商好
优点：集中控制 优先级 Q0S 信道利用率（无冲突） 无缝切换
缺点：集中控制 高代价：开销大，需要预留一个占很大一部分的带宽；OFDMA微秒级的同步技术，依赖基站精准的时钟同步。

## Slide 4: Wi-Fi: Implicit Control
Is anyone transmitting?
No. Let’s go!
Is anyone transmitting?
Yes. I must back off.
1 Mississippi,
2 Mississippi…
Data Plane
Data Plane
Data data data data
Data data data data
Hidden Node
Data data data data
Collision
File Sync
VoIP
Notes: implicit隐式控制CSMA
Explicit显式控制RTS/CTS
优点：简单，即插即用
缺点：低效 碰撞
这里要讲解一下隐藏终端 带来碰撞 为了解决这个问题 提出了 RTS：请求发送

## Slide 5: The Challenge: the Best of Both Worlds
Data data data data
I want to transmit
Can we get the benefits of centralized control?
While retaining Wi-Fi’s asynchronous and distributed properties
Without designating spectrum

## Slide 6: Flashback
Flashback is a decoupled, lightweight control plane
  Decoupled: send control messages concurrently with data messages on the same channel
  Lightweight: barely impacts network performance (<1% packet loss)
  Control Plane: enables rich set of applications (efficient scheduling, QoS enforcement, power savings, fast association, etc.)

## Slide 7: How can we send control messages without interfering with data packets?
Data data data data
Flash

## Slide 8: OFDM is a Grid
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
0
1
2
3
60
61
62
63
Subcarrier Position
…
…
…
0
4
8
12
16
Time []
20 MHz
Notes: OFDM即正交频分复用技术
将信道分成若干正交子信道，将高速数据信号转换成并行的低速子数据流，调制到在每个子信道上进行传输

## Slide 9: Redundancy Protects from Errors
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol
Symbol | Symbol
Symbol | Symbol
Symbol | Symbol
Symbol | Symbol
Symbol | Symbol
Symbol | Symbol
Symbol | Symbol
Symbol | Symbol
Symbol | Symbol
Wi-Fi Packet
Symbol | Error | Symbol | Symbol
Error | Error | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Error
Symbol | Symbol | Symbol | Error
Symbol | Symbol | Symbol | Error
Symbol | Symbol | Symbol | Error
Symbol | Symbol | Symbol | Symbol

## Slide 10: Rate Adaptation Adds Redundancy
Rate adaptation trades off redundancy and throughput
  Redundancy is added in significant discrete chunks
  Dropping a packet is very costly
Rate adaptation errs on the conservative side
Notes: 编码率越高 比特率越高 SNR越大 鲁棒性越差

## Slide 11
Notes: SNR 信噪比即放大器的输出信号的电压与同时输出的噪声电压的比 设备的信噪比越高表明它产生的杂音越少。
Link Margin 链路容限
是SNR的真实测量值与理论值的一个差值。
产生的原因：
SNR 毫秒级的 变动 很难测量，因此如果要计算发送的速率也是会有误差，所以实际发送过程中会以低于理论值的比特率发送。这样便会产生link margin。

## Slide 12: Exploiting Margin
  Key insight: intentionally interfere
  Leverage OFDM grid structure
    Localize interference in the OFDM grid
  Flashes: high powered single subcarrier signal
    Single frequency sinusoid on particular time slot
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Flash | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Flash | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Notes: Instead of sending a regular OFDM packets over the entire band, the control message transmit-ter sendsflashes. （不是整个频段） 把影响降低到某个局部 而不是整个频段

## Slide 13: Receiver Detects Flashes in Parallel
Flashes are easy to detect at receiver
  Power spike on single subcarrier
Erase flashes from data packet
Decode flash and data packet in parallel
Flash
Notes: 由于时钟不是同步的，因此接收端有可能接收到的 峰值 是跨在两个时间段上。

## Slide 14: How is the Control Message Encoded?
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Flash | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Flash | Symbol | Symbol
Flash | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
Symbol | Symbol | Symbol | Symbol
0
1
2
3
60
61
62
63
…
…
…
0
4
8
12
16
Time []
Subcarrier
Messages encoded by relative distance between consecutive flashes
  Each digit is relative distance
  Digit 1: 60 – 3 = 57
  Digit 2: 62 - 60 = 2

## Slide 15: Practical Concerns
Flash transmitter is not synchronized to receiver
  CFO problem solved using relative frequencies
  Time sync problem solved by detecting flashes at whole and half samples
AGC
  Commodity ADCs have sufficient dynamic range to accommodate both data and flashes
Notes: CFO carrier frequency offset 载波频率便宜

## Slide 16: Implementation
Implemented OFDM PHY supporting Flashback
  Receiver + transmitter
Implementation using NI Virtex-5 LX30 FPGA based software radios
  Designed with LabVIEW

## Slide 17: Transmitter Implementation
Encoder
Modulator
64 IFFT
Cyclic Prefix
Flash Encoder
DAC
Data Packet
Control Message
MUX

## Slide 18: Receiver Implementation
ADC
Sync
64 FFT
Equalizer
Demodul-ator
Flash Decoder
Flash Eraser
Flash Detector
Viterbi Decoder
Data Packet
Control Message
Modular, requires minimal changes

## Slide 19: Maximum Flash and Data Rate
50,000 flashes per second
175 kb/sec
125,00 flashes per second
400 kb/sec
Chart: Flashes per Second
| 2500 | 5000 | 6250 | 12500 | 25000 | 50000 | 125000
Overall Packet Loss Rate of Data Plane, Quiet Environment | 0.1806 | 0.7818 | 0.8006 | 0.889 | 0.9272 | 0.925 | 2.0126
Overall Packet Loss Rate of Data Plane, Typical Noisy Environment | 0.0803 | 0.1339 | 0.1345 | 0.1779 | 0.179 | 0.1809 | 0.8406

## Slide 20: Flashback-MAC
Demand Map |  | 
Node 5 | 150 KB | Bulk Transfer
Node 1 | 20 KB | Low Latency
Demand Map |  | 
Node 5 | 150 KB | Bulk Transfer
Flash
Flash
Node 1
Node 5
ACK + piggyback
Data Data Data Data
Data Data Data Data

## Slide 21
Chart: Flashback-MAC's Throughput Improvement vs. Wi-Fi
CSMA/CA 20-80% Uplink-Downlink Data Traffic | 3.6439 | 3.8484 | 4.0709 | 3.7716 | 3.7831 | 3.8313 | 4.194 | 4.1786 | 4.1633 | 4.1183 | 4.0723 | 4.053 | 4.0335 | 4.0941 | 4.1562 | 4.1612 | 4.1663 | 4.2144 | 4.2628 | 4.3128
CSMA/CA 100-0% Uplink-Downlink Data Traffic | 1.3426 | 3.5104 | 4.4634 | 4.9369 | 5.1632 | 4.6428 | 4.8277 | 5.1244 | 4.9942 | 5.0603 | 5.7294 | 5.5488 | 5.4516 | 5.5022 | 5.5502 | 5.6411 | 5.6816 | 5.6096 | 5.5586 | 5.5689
RTS/CTS, 20-80% Uplink-Downlink Data Traffic | 1.3138 | 1.3117 | 1.3888 | 1.4763 | 1.5282 | 1.5838 | 1.6072 | 1.6312 | 1.6374 | 1.6437 | 1.6361 | 1.6287 | 1.6516 | 1.6749 | 1.6656 | 1.7571 | 1.7621 | 1.767 | 1.7575 | 1.7568
RTS/CTS 100-0% Uplink-Downlink Data Traffic | 1.3335 | 1.3611 | 1.3894 | 1.3887 | 1.3687 | 1.3851 | 1.4413 | 1.4875 | 1.5458 | 1.5876 | 1.5865 | 1.6051 | 1.6135 | 1.6219 | 1.6255 | 1.6303 | 1.6278 | 1.6263 | 1.7177 | 1.8176
Centralized scheduling  4X throughput
Notes: RTS/CTS协议，即请求发送，允许发送协议。相当于一种握手协议。主要用来解决隐藏终端的问题。
隐藏终端：基站A向基站B发送信息，基站C未侦测A也向B发送，所以A和C同时将信号发送到B，引起信号冲突。
A向B发送RTS信号，表明A要向B发送若干数据，B收到RTS后向所有基站发送CTS信号，表明已经准备就绪，其余基站 按兵不
动 然后A 向 B发送数据。最后 B 接收完数据后向所有基站广播 ACK确认帧。
RTS/CTS的缺点：发送这类控制包需要一个可靠的方式，即低比特率发送，于是占用了信道时间；另外在拥塞的网络 Qos 也不能很好的保证，因为这些控制信息是包含在数据通道上。于是很多管理员都不启用这个协议

## Slide 22
Chart: Percentage of Channel Time Used for Transmitting Data
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Flashback-MAC, 20-80% Uplink-Downlink Data Traffic | 91.2 | 91.3026 | 90.9076 | 90.5126 | 90.6382 | 90.7639 | 90.6668 | 90.5696 | 90.4764 | 90.3831 | 90.276 | 90.169 | 90.4489 | 90.7288 | 90.3827 | 90.0366 | 89.9412 | 89.8457 | 89.6592 | 89.4727
Flashback-MAC, 100-0% Uplink-Downlink Data Traffic | 92.828 | 93.4762 | 94.1244 | 92.6507 | 91.177 | 92.1276 | 93.0783 | 93.1819 | 93.2855 | 92.1605 | 91.0355 | 91.0355 | 91.0355 | 91.0355 | 91.0355 | 91.0971 | 91.1587 | 91.273 | 91.3874 | 91.3874
CSMA/CA 20-80% Uplink-Downlink Data Traffic | 82.678 | 85.1668 | 83.9578 | 82.7488 | 80.6465 | 78.5442 | 79.335 | 80.1258 | 79.79 | 79.4542 | 78.7401 | 78.026 | 77.838 | 77.6501 | 77.7598 | 77.8696 | 76.8956 | 75.9215 | 76.5992 | 77.2768
CSMA/CA 100-0% Uplink-Downlink Data Traffic | 83.1261 | 86.9167 | 85.9757 | 85.2568 | 82.9198 | 80.311 | 78.967 | 81.9544 | 81.9798 | 79.6836 | 79.1104 | 79.0995 | 78.0273 | 77.6695 | 78.0459 | 78.0651 | 77.0856 | 76.296 | 76.5811 | 76.6306
RTS/CTS, 20-80% Uplink-Downlink Data Traffic | 69.4188 | 69.6087 | 65.4593 | 61.3098 | 59.3086 | 57.3073 | 56.4146 | 55.5219 | 55.255 | 54.9881 | 55.1769 | 55.3609 | 54.7645 | 54.17 | 54.2648 | 51.2423 | 51.0419 | 50.8461 | 51.0161 | 50.9283
RTS/CTS, 100-0% Uplink-Downlink Data Traffic | 69.6132 | 68.6792 | 67.7451 | 66.7157 | 66.6149 | 66.5141 | 64.5796 | 62.6451 | 60.3472 | 58.0493 | 57.3824 | 56.7155 | 56.422 | 56.1285 | 56.0033 | 55.8782 | 56.001 | 56.1239 | 53.2022 | 50.2805
Decoupled Control = High Utilization

## Slide 23
Chart: Queue Latency of Priority Traffic
| 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
Flashback, 100% Uplink Traffic, 2 Latency Sensitive Nodes | 0.7347 | 0.71007 | 0.64651 | 0.67831 | 0.64743 | 0.63436 | 0.63086 | 0.6261 | 0.63441
CSMA/CA, 100% Uplink Traffic, 2 Latency Sensitive Nodes | 8.2027 | 230.7597 | 585.847 | 1150 | 1033.93 | 1329.2 | 1544.17 | 1700.255 | 1953.26
RTS/CTS, 100% Uplink Traffic, 2 Latency Sensitive Nodes | 1.7204 | 3.755 | 26.6949 | 25.5777 | 73.5834 | 255.407 | 438.286 | 590.859 | 615.5
Flashback enforces QoS in extreme scenarios

## Slide 24: Broader Implications of Flashback
Decoupling is key property of Flashback
Enables hitherto impossible applications
  Power duty cycling
  Fast association
  Coexistence across networks
  Peer discovery
  …

## Slide 25: Summary
What: Flashback is a decoupled lightweight control plane
How: Cause localized interference to send control messages
Why: Centralized scheduling facilitates many applications